## Slide 1
ME2 — “Alexa” Voice Command Model (VCM)
Offline speech-to-intent on the edge · no cloud round-trip
17 October 2026 · King James Villasin · AI 231 MLOps, UP · Model · Dataset · Training on A100 · Validation on RPi 4
p. 1 / 3
Model
Mic · 16 kHz → log-Mel 40 × ≤500 frames
Causal DS-CNN encoder × 5 res blocks · 256-dim
streaming · 40 ms steps · ~1.9 s receptive field
CTC head · 120 tokens
Grammar (beam search) → intent + slot
Actuator · web dashboard
· Onikuma microphone · Tronsmart Halo 200 speaker
Raspberry Pi 4
Item | Value
Parameters / weights | 951,672 (0.95 M) · 3.8 MB fp32 ONNX
Validation on the Raspberry Pi 4
Item | Value
Keyword / intent acc | 82.7 % (167/202) / 73.3 % (148/202)
False-accept rate | 12.5 % (2 / 16 out-of-scope clips)
Latency p50 / p95 | 617 ms / 1,193 ms
RTF p50 / p95 | 0.0066 / 0.012
VCM inference | 12.3 ms mean · 16.0 ms p95 per command
Runtime | onnxruntime 1.21 · CPU · 4 threads
Live over-the-air run on the 202-clip ME2 holdout (+16 without wake word).
Dataset
Item | Value
Source | AI231 ME2 Voice Commands + PLD (English) + Common Voice (Asian-accented)
Hours / utts | 21.9 / 9.4 · 46,436 / 19,986
Speakers | Synthetic and real voices, 70 / 30 split
Labels | 19 intents + out-of-scope · 93 commands · 118-word vocab
Training on the A100 cluster
Item | Value
Cluster | 2 × A100-SXM4-40GB · DDP · bf16
Objective | CTC (blank = token 119)
Optimiser | AdamW · lr 2.83e-3 · one-cycle
Epochs / F1 | Best 309 of 459 · token F1 0.894
Wall-clock | ~1 h 51 min (~3.5 A100-hours)
Wake word vs VCM
Stage | Accuracy (Live on Pi) | Lost Trials
Wake Word | 82.7% (167/202) | 31
VCM | 86.2% (144/167) | 23
Wake + VCM | 73.3% (148/202) | 54
Notes: Source: github.com/trueshotjames/me2-vcm README §3, §5, §7 and benchmark run 20261017-015001. Live Pi accuracy covers wake word + VCM together.

## Slide 2
ME2 — Wake Word Model (“Alexa”)
Always-on keyword spotting on the edge · no cloud round-trip
17 October 2026 · King James Villasin · AI 231 MLOps, UP · Model · Dataset · Training on A100 · Validation on RPi 4
p. 2 / 3
Model
Mic · 48 → 16 kHz · raw waveform 1.5 s (24,000 samples)
Learned conv front end + 3 DS-conv blocks · 128-dim
scores the latest 1.5 s every 0.2 s
Wake head · sigmoid, threshold 0.5
Triggers the VCM
Raspberry Pi 4
Item | Value
Parameters / weights | 33,613 (33.6 k) · 57 KB int8 ONNX
Validation on the Raspberry Pi 4
Item | Value
Keyword acc | 82.7 % (167 / 202 trials)
False-accept rate | 31.2 % (5 / 16 trials without wake word)
Runtime | onnxruntime 1.21 · CPU · int8
Same live run: one recorded “Alexa” take before each ME2 holdout clip, plus 16 commands without it.
Dataset
Item | Value
Source | SynTTS-Commands (“Alexa” + 15 other commands) + Speech Noise Dataset
Hours / utts | 4.54 / 1.14 h · 13,796 / 3,449
Speakers | CosyVoice 2 clones of VoxCeleb voices
Labels | 2 classes · wake / not wake
Training on the A100 cluster
Item | Value
Cluster | 2 × A100-SXM4-40GB · DDP
Objective | Binary cross-entropy
Optimiser | AdamW · lr 2.83e-3 · one-cycle
Epochs / F1 | Best 130 of 180 · val F1 0.984 (acc 0.987)
Wall-clock | ~1 min 41 s (preprocess 15 s, train 86 s)
Notes: Source: github.com/trueshotjames/me2-vcm README §3, §5, §8; data and logs on Hugging Face trueshotjames/ai231-king-me2 (v1.0). Wake latency was not measured separately.

## Slide 3
To Be Submitted
GitHub repository | github.com/trueshotjames/me2-vcm · public · MIT licence
Dataset location | Hugging Face trueshotjames/ai231-king-me2 (tag v1.0) · DOI 10.57967/hf/10994 · CC BY-NC 4.0; third-party clips keep their own terms
A100 cluster | Node ai-n002 · 2 × A100-SXM4-40GB · VCM ~1 h 51 min, wake ~1 min 41 s · seed 1234
Model weights | GitHub releases v0.1-vcm (VCM) and v1.0 (wake): ONNX + PyTorch · CC BY-NC 4.0
What the reviewer will look for
# | Item | Status
1 | Repo public, one-command reproduction | Done · python run_train_pipeline.py
2 | Dataset licensed and citable (DOI) | Done · CC BY-NC 4.0 · DOI 10.57967/hf/10994
3 | Training logs + final checkpoint committed | Done · logs on HF, checkpoints in GitHub releases
4 | Pi 4 latency reproduced by the posted script | Done · run_benchmark.sh, results in benchmark_results/
5 | Held-out test set, unseen speakers | Done · 202-clip ME2 holdout, speaker-disjoint
6 | Baseline of comparable size compared | Done · README §3 (published numbers, not re-run)
p. 3 / 3